Name: _____________________________________________ Date: _________________ Period: _____

Electricity and Magnetism Study Guide

Test Date: Tuesday March 28, 2017

| 1. Positive charges __________________ positive charges __________________ negative charges | Repel & Attract |
| --- | --- |
| 2. You rub a balloon on carpet. When you hold it next to a wall, the balloon is attracted to the wall, why? | Because rubbing creates a negative charge that is carried by electrons. The electrons can build up to produce static electricity. Therefore the balloon sticks to wall because a negative charge instead of a neutral charge. |
| 3. In an electrical circuit what does voltage do for electrons? | Voltage is a measure of the energy carried by the charge. Voltage attempts to make a current flow, and current will flow if the circuit is complete. |
| 4. What is the difference in direct current and alternating current? | Direct current is only one pathway and alternating current has multiple pathways. |
| 5. What is current in an electrical circuit? | The flow of electrons along a complete, closed path |
| 6. What is a conductor? | Materials that allow electricity to flow easily through them. |
| 7. What are some examples of conductors? | Examples: iron, cobalt, nickel, copper, WATER |
| 8. What are insulators? | A material or an object that does not easily allow heat, electricity, light, or sound to pass through it. Examples: plastic, rubber, wood |
| 9. What does resistance do in a circuit? | Resistance is the friction in an electrical circuit that controls the flow of current. |
| 10. What are the units of measure for: Resistance Current Voltage | Resistance: Ohms Current: Amps Voltage: Volts |
| 11. In a series circuit, 1 ampere of current passes through the light bulb. The resistance of the light bulb is 3.0 ohms. What is the voltage of the battery? | V = I x R V = 3 volts |
| 12. What is the current in a circuit, if the total resistance of the circuit is 9 ohms and the voltage is 9 volts? | I = V/R I = 1 amps |
| 13. Household appliances are powered by which type of current? | Alternating Current (AC Current) |
| 14. Battery powered appliances are by which type of current? | Direct Current (DC Current) |
| 15. A positively charged object comes into contact with a neutral object. Explain the flow of charges. | The positively charges object comes into contact with a neutral object and neutral object becomes positively charged and the original positively charged object is less powerful than before. |
| 16. After rubbing your hair with a balloon your hair stands up. Now you hold the balloon near a wall and it sticks to the wall. Which is an example of friction? | The example of friction is rubbing your hair with the balloon. |
| 17. After rubbing your hair with a balloon your hair stands up. Now you hold the balloon near a wall and it sticks to the wall. Which is an example of induction? | The example of induction is holding the balloon near the wall and it sticks to the wall. |
| 18. A neutral metal object is touched by a negatively charged object. Where do the electrons travel to and what will the charge of the metal object be? | The new charge of the neutral metal object will become negatively charged. |
| 20. Describe the flow of electrons in a parallel circuit that has one battery and two branches. | The flow of electrons will remain constant throughout both branches (pathways) of the circuit. |
| 21. What happens to the current in a circuit if you increase the resistance? | If the resistance in a circuit is increased the current will decrease |
| 22. How could you increase the current in a circuit? | Increase the size of the battery |
| 23. What are the advantages of electromagnets over permanent magnets? | The strength of an electromagnet can be adjusted by the amount of electric current allowed to flow into it. An electromagnet’s magnetic field can be rapidly manipulated over a wide range by controlling the amount of electric current supplied to the electromagnet. |
| 24. What forces allow electric motors to turn? | Electrical and magnetic forces |
| 25. What are the parts of an electromagnet? | Power source, copper wire, and ferromagnetic material |
| 26. How can you increase the strength of an electromagnet? | By increasing the volts of a power source and/or increasing the number of coils wrapped around the ferromagnetic material |

Directions: Complete the following equations using Ohm’s Law.

1. What is the current in a 25V circuit if the resistance is 8Ω?

I = 3.1 Amps

2. What voltage is required to move 2A through 5Ω?

V = 10 V

3. What voltage is required to move 2A through 10Ω?

V = 20 V

4. What is the current in a 240V circuit if the resistance 20Ω?

I = 12 Amps

5. What is the current in a 120V circuit if the resistance 10Ω?

I = 12 Amps

6. What is the current in a 120V circuit if the resistance 5Ω?

I = 24 Amps

7. What is the resistance of a circuit with 20V and 2A?

R = 10 Ohms

8. What is the resistance of a circuit wit 120V and 1A?

R = 120 Ohms